a line-tracking mouse

ENGINEERING ASSIGNMENT

| WHAT YOU DO |  | You research and build a Line-Tracking Mouse. This is an intelligent robotic mouse which tracks a black line using three photo interrupters in its ‘eyes’. You will have to select all the components, tools, and equipment yourself. Having constructed the mouse, you will have to test it against a specification, race it, conduct research and make recommendations on suitable modifications to make it go faster and increase its marketability. |
| --- | --- | --- |
| EQUIPMENT AND MATERIALS |  | Components for a Line Tracking Mouse A computer with access to the internet. Tools for constructing electronic circuits A Multimeter for testing electronic circuits |
| QUALIFICATION UNITS |  | GCSE Engineering Unit 2: Engineered Products |

| TASK 1 |  | Gantt Chart Use a computer to create a Gantt Chart Table similar to the one shown in the Information Sheet Gantt Chart for Design, which is part of this assignment. |
| --- | --- | --- |
| TASK 2 |  | Components and equipment Use the Parts List and assembly diagram to select all the components required to build the Mouse from the stores area. Select the tools and equipment you will need to construct and test the Mouse from the workshop. |
| TASK 3 |  | Build the Mouse Follow the assembly diagrams to build the mouse. |
| TASK 4 |  | Research Research methods of improving the performance of the Mouse. This will include battery technology, and materials. Follow the instructions on the Task Sheet Line-Tracking Mouse: Research. |
| TASK 5 |  | Production Plan You must use a computer to create a Production Plan. Consult the separate Information Sheet Production Plan. |
| TASK 6 |  | Method Statement You must produce a written Method Statement document that details exactly how to carry out each stage of the Production Plan, listing the necessary tools, equipment, parts, relevant Health and Safety issues, and the quality control points during the construction of the Line Tracking Mouse. You must use relevant drawings and images to enhance your description. It is essential that the document is grammatically correct and your meaning is clear to the reader. |
| TASK 7 |  | Specification for Testing Line Tracking Mouse As the Line Tracking Mouse has no technical specification one will have to be created to provide a benchmark for testing purposes once your Mouse has been completed so it can be compared against this. Follow the instructions on the Information Sheet: Suggested Specification for Testing Line-Tracking Mouse. |
| TASK 8 |  | Testing To test the Line-Tracking Mouse you will need to design a track layout made from black electrical tape to be fixed on a flat board 60cm to 1 metre in width by 2 to 3 metres in length that will allow you to carry out a series of trials to find out its maximum and average speeds, and its turning capability with different types of batteries. The layout should have at least two tracks of equal length that allow timed races to be carried out. You must allow at 2.1 metres on each side of the board for spectators. Evidence must be submitted showing clearly how you calculate the area of the board and the minimum area of the room required. Produce a scaled drawing of the track layout and room. You must provide written evidence of how you tested the Line Tracking Mouse against the specification. You must carry out at least 20 speed runs to calculate: the average speed the range of speeds of the Line Tracking Mouse. The results must be presented in an appropriate form with correctly labelled axes. You must describe what your results tell you about the Mouse’s performance. Produce a written description of the testing against the specification. |
| TASK 9 |  | Increasing the Speed Follow the instructions on the Task Sheet; Increasing the Speed to see if you can improve the performance of your mouse before the race. Explain to a group of students what steps you have taken to increase the speed. Be prepared to answer questions and discuss the issues with your audience. Your talk should last at least four minutes. |
| TASK 10 |  | Race Now that you have tested and tuned your Line Tracking Mouse there will be a competition to find the fastest Mouse within your group of students. Write a newsletter that describes the competition as part of the evidence for your portfolio. |
| TASK 11 |  | Components List Part of an engineer’s job involves selecting and ordering components for projects and analysing the costing totals. Create a spreadsheet for re-ordering ALL the component parts for the Line Tracking Mouse with columns headed Quantity Description Supplier Reference Code Price for each component Minimum component order price The spreadsheet should be created with an equation to calculate the total cost of the Line Tracking Mouse components the Total Cost including VAT the percentage cost of a part against the total cost. Finally you should breakdown the costs into four areas: electrical and mechanical components batteries wheels gearboxes which should be displayed as a bar graph or a pie chart. |
| TASK 12 |  | Increasing Sales You must research and develop ways of increasing the sales of the Line-Tracking Mouse. You could do the following: Research using questionnaires and discussions about what customers would like Use your IT skills to analyse the data and summarise the results Decide on the best options and give your reasons. Generate ideas, sketches, shapes and names for your Line Trackers. Create a poster with images and text to advertise the Line Tracker Use your IT skills to generate other marketing ideas Create a poster with images and text to advertise the Line Tracking Mouse Race Create a sponsorship letter to try and generate support for the Race. |

| INFORMATION SHEET |
| --- |
| GANTT CHART FOR LINE-TRACKING MOUSE |
| STUDENT NAME |  |  |
|  | WEEK 1 | WEEK 2 | WEEK 3 | WEEK 4 |
| Checking Parts |  |  |  |  |
| Up to Board Assembly |  |  |  |  |
| Main Board Assembly |  |  |  |  |
| Gear Box Assembly |  |  |  |  |
| Gear Box Testing |  |  |  |  |
| Assembly of Main Parts |  |  |  |  |
| Quality Control Tests |  |  |  |  |
| Testing Mouse against the specification |  |  |  |  |
| Research improvements to the design |  |  |  |  |
| Research sales improvements |  |  |  |  |

TASK SHEET

LINE-TRACKING MOUSE: RESEARCH

As part of your research into the Line Tracking Mouse investigate one of the following “How a Battery Works” at www.howstuffworks.com and www.bbma.co.uk . Produce a written summary of what they say. Research microcontrollers at www.rev-ed.co.uk and summarise what is said about microcontrollers at the beginning of the PICAXE Manual found under the Data sheet heading, and at www.howstuffworks.com to summarise what is said about microcontrollers in the section headed Electronics. Now visit www.duracell.com/oem/ and look at the Alkaline Manganese MX1500 1.5V AA battery. Make some notes about the graph of discharge characteristics. Now go to the www.energizer.com website and look for the Energizer E91 1.5V AA Alkaline battery. Look at the graphs for the discharge “Industry Standard Tests” and compare the results with those for the MX1500. Provide a written summary of what the graphs show. Research also the materials used in making the Line-Tracking Mouse, and write a report which summarises why they have been used rather than others. For example, why the gear wheels are made of plastic rather than metal. a. Printed Circuit Boards b. Solder c. Flux Cleaner d. Battery and motor holders e. Gears f. Electrical wiring & sockets g. Mouse base h. Resistors

INFORMATION SHEET

SUGGESTED SPECIFICATION FOR TESTING LINE TRACKING MOUSE

Number & Type of Batteries used: ____________ Battery (Ah rating) : _________ Max. Current Consumption: _______ Maximum D.C. Supply Voltage: _____________ Normal Mouse Running Time: __________ Weight (no batteries): _______gm Weight (with batteries) _____gm Maximum Height: ______ cm Maximum Width: __________ cm Maximum Length: __________ cm Max. Track Width: ________cm Min. Track Width: _______cm SPEEDS MUST BE BASED ON AT LEAST 20 TEST RUNS Maximum Speed: _________ Feet per second __________ mph Maximum Speed: _________ Metres per second _________Km/hr Minimum Speed: __________ Feet per second __________mph Minimum Speed: __________ Feet per second __________mph Average speed: ___________ Feet per second _________mph Average speed ___________ centimetres per second _______Km/hr Minimum Turning Circle Diameter: _____________________.

TASK SHEET

INCREASING THE SPEED

Use the following information to calculate the speed of your Line Tracking Mouse and make recommendations on how to increase the speed. You must provide practical evidence to prove your theory. MOUSE WHEEL DIAMETERS INCLUDING TYRES = 35.75mm MOTORS 8,000 rpm GEAR RATIO: 10T/36T x 14T/36T x 14T/36T x 14T/36T 36 36 14 Wheel Diameter 36 35.75mm 14 14 10 14 14 36 (number of teeth on each gear wheel) Motor Shaft (8000rpm)

key skills

LINE-TRACKING MOUSE ASSIGNMENT

| STUDENT’S NAME |  |
| --- | --- |

| KEY SKILLS COVERED This assignment addresses the skills highlighted in bold type. Circle those which have been achieved by the student. | LEVEL 1 |
| --- | --- |
|  | C1.1.1 |  | N1.1.1 |  | ICT1.1.1 |
|  | C1.1.2 |  | N1.1.2 |  |  |
|  | C1.2.1 |  | N1.2.1 |  | ICT1.2.1 |
|  | C1.2.2 |  | N1.2.2 |  | ICT1.2.2 |
|  | C1.2.3 |  |  |  |  |
|  | C1.3.1 |  | N1.3.1 |  | ICT1.3.1 |
|  | C1.3.2 |  | N1.3.2 |  |  |
|  | C1.3.3 |  | N1.3.3 |  |  |
|  |  |  | N1.3.4 |  |  |
|  | LEVEL 2 |
|  | C2.1a.1 |  | N2.1.1 |  | ICT2.1.1 |
|  | C2.1a.2 |  | N2.1.2 |  |  |
|  | C2.1a.3 |  | N2.1.3 |  |  |
|  | C2.1b.1 |  |  |  |  |
|  | C2.1b.2 |  |  |  |  |
|  | C2.1b.3 |  |  |  |  |
|  | C2.2.1 |  | N2.2.1 |  | ICT2.2.1 |
|  | C2.2.2 |  | N2.2.2 |  | ICT2.2.2 |
|  | C2.2.3 |  |  |  |  |
|  | C2.3.1 |  | N2.3.1 |  | ICT2.3.1 |
|  | C2.3.2 |  | N2.3.2 |  | ICT2.3.2 |
|  | C2.3.3 |  | N2.3.3 |  |  |
|  | C2.3.4 |  | N2.3.4 |  |  |

| COMMENTS |  |
| --- | --- |

teacher’s notes

LINE-TRACKING MOUSE ASSIGNMENT

|  |  | The Line-Tracking Mouse kit of parts can be bought from Rapid Electronics Ltd., Severalls Lane, Colchester, Essex CO4 5JS. Telephone 01206 751166. Website: www.rapidonline.co.uk . Its order code is 13-1035, price £8.99 +VAT (Price correct at June 2006). An extract of the Assembly Diagram is attached below to indicate the nature of the task. Take the kits apart and put the components into a stores area, so that students select what they need from the stores area using the assembly diagram. The mouse-racing section of this assignment can be used to generate general interest, even media interest, in the engineering course, as indicated in the examples of newspaper articles below. |
| --- | --- | --- |
| POSSIBLE VARIATIONS |  | The Communications and Application of Number aspects of the assignment could be extended as follows. The racing room For this part of the assignment students are required to measure their track board, then allow 2.1 metres on all sides for spectators. Typical questions could include: Calculate the minimum size room, which would be required for this. Calculate the area of the track board. Calculate the floor area of the room. Calculate the ratio of the area available for spectators to the area of the track board. Draw a scale drawing of the room with the track board in place. What percentage of the total area of the room does the track board take up? Draw a scale diagram the room, with the track board in position. Assuming that the room will be 2.7m high, calculate the volume of the room. How could you check your volume was correct? How about suggesting that for Level 2 they design a circular room to meet the requirements and calculate the area and volume of the room? For Level 1 some guidance would need to be given for some of the calculations and the questions for Level 2 would need to be less straightforward than for Level 1. Sponsorship Imagine that you are the secretary of your school / college line tracking mouse racing club. In this task you will write in business letter format a letter to a local company asking them if they would be willing to provide a trophy for your forthcoming time trial event. To complete this task you should first create a letterhead for your club, using both text and image. Use your letterhead to write to a local company to ask if they would be willing to sponsor your club by providing a trophy for the coming time trials. Explain in the letter how in return for providing the trophy they will gain valuable advertising for their company. The letter should be in business letter format. Time Trials The results from 10 timed runs (level 1) or 20 timed runs (level 2) will be used to calculate the mean and the range. In addition students could be asked to comment on such areas as: How can you check that your mean makes sense? Is there a difference between battery types? Which mouse performed the best? If two or more drivers used the same mouse was there a difference in the drivers? Was there a difference between the two (or more) different tracks? If so could you suggest why? Costing The costing is developed in spreadsheet format as detailed in the assignment. In order to satisfy the key skill requirements the students could be asked to answer further questions, such as: Calculate the total price + VAT. How would you check that your percentages for the individual components are correct? Work out the ratio of electronic components : mechanical components. Describe what the bar chart shows. Newspaper report Write an article for your school / college student newspaper. This could take the form of a report on the time trials, taking into consideration the age of your readers. You could include information on subjects such as the drivers, the sponsors of the event, details of the mice etc. Grammar and spelling must be accurate. It would be helpful to provide an image to make the article more interesting for your readers. |

LINE-TRACKING MOUSE EXTRACT FROM ASSEMBLY DIAGRAM

LINE-TRACKING MOUSE EXAMPLE OF PRESS COVERAGE

LINE-TRACKING MOUSE EXAMPLE OF PRESS COVERAGE